## Slide 1: Status of the XENONnT Dark Matter Search Experiment
CoSSURF 2022 - May 13, 2022
Shengchao Li li4006@pudue.edu
ON BEHALF OF

## Slide 2
Shengchao Li | CoSSURF 2022 | May 13, 2022
2
XENON Collaboration
~170 scientists

## Slide 3
Redundant signals for each event
  prompt scintillation light (S1)
  delayed signal from charge extracted into gas phase (S2)
Full 3D position reconstruction
  x-y from PMT hit pattern
  z from drift time
Discrimination between electronic recoil (ER) vs. nuclear recoil (NR)
  charge to light ratio (S2/S1)
Shengchao Li | CoSSURF 2022 | May 13, 2022
3
XENON Dual-phase Time Projection Chamber

## Slide 4
XENON10 | XENON100 | XENON1T | XENONnT (predicted)
2005 - 2007 | 2008 - 2016 | 2012 - 2018 | 2019 - 2026
14 kg Xe | 62 kg Xe | 2 tonne Xe | 5.9 tonne Xe
~10-43 cm2 | ~10-45 cm2 | ~10-47 cm2 | (~10-48) cm2
~2M background ER events/(keV t y) | 1800 background ER events/(keV t y) | 82 background ER events/(keV t y) | (2) background ER events/(keV t y)
4
Shengchao Li | CoSSURF 2022 | May 13, 2022
4
XENON Time Projection Chambers (TPCs)
Laboratori Nazionali del Gran Sasso (3400 m.w.e)

## Slide 5
PRL 119, 181301 First DM results
PRL 121, 111302 One ton × year WIMP search
PRL 122, 141301 Spin-dependent WIMPs
PRL 122, 071301 WIMP-pion interaction
PRD 103, 063028 Inelastic scattering
PRD 102, 072004 Low energy ER excess
PRL 123, 251801 S2-only DM search
PRL 123, 241803 Light DM via Migdal
Nature 568, 2019 2 double electron capture
PRL 126, 091301 8B solar neutrino
..and more to come
(data taken 2016-2018)
3.3 sigma excess
Shengchao Li | CoSSURF 2022 | May 13, 2022
5
Scientific Results from XENON1T

## Slide 6
JCAP 11 (2020) 031
  To gain more than 1 order of magnitude in DM sensitivity:
    Larger fiducial volume
    Low electron recoil background
    Low neutron induced background
4 tonne
1/6 of XENON1T SR1 level
1 event in 20 ton × year exposure
Shengchao Li | CoSSURF 2022 | May 13, 2022
6
Upgrade from XENON1T to XENONnT

## Slide 7
  Tunable field shaping rings
  Minimal use of PTFE to reduce material background
Larger TPC than XENON1T
  Active Xe mass 2t -> 5.9t
  Drift length 1m -> 1.5 m
  PMTs 248 -> 494
Improved surrounding systems
  Two calibration tubes
  One neutron generator pipe
  Neutron veto system
M uon veto system
Larger detectors need a higher purity to reach the same level of charge collection
3x
1.5x
2x
Shengchao Li | CoSSURF 2022 | May 13, 2022
7
XENONnT Detector Upgrades

## Slide 8
SAES
getter x2
Magnetically coupled piston pumps for complete isolation
Clean components with (330 ± 60) μBq Rn emanation rate
Xe flow 100 slpm
1.5 bar at MagPump inlet
Two pumps for redundancy
noble gas
drive
EPJC 78 (2018) 604
piston
Piston chamber
Rn clean gaskets
Shengchao Li | CoSSURF 2022 | May 13, 2022
8
GXe Purification System

## Slide 9
 | Max drift time | Electron lifetime | e- surviving full drift
XENON1T | 0.67 ms | 0.65 ms | 30%
XENONnT | ~2 ms | >10 ms | 80%
Two sets of customized filters:
  ultra-low radon level
  replaceable/regenerable
Purity monitoring with a dedicated device via electron lifetime
High flow of 2 LPM (=350 kg/h) :
  electron lifetime reached 5 ms in 5 days
  over time stable at >10 ms
with 8.5t Xe in cryostat
Shengchao Li | CoSSURF 2022 | May 13, 2022
9
LXe Purification System
Notes: The 1.5 times longer drift length demands improvements in removing electronegative impurities that dampen the S2 signal
Electron lifetime ∝ electronegative impurities
need to vaporize or use a heat exchanger

## Slide 10
Radiogenic neutrons
Cosmogenic neutrons
CEνENs from Atm+DSN and solar neutrinos
XENONnT projection
222Rn emanation from material
85Kr from natural krypton
Xe isotopes: 124Xe ECEC and 136Xe 2 decay
Solar neutrinos
Distillation
Distillation + Radiopurity
Neutron Veto
Muon Veto
JCAP 11 (2020) 031
Electronic Recoil
Nuclear Recoil
Shengchao Li | CoSSURF 2022 | May 13, 2022
10
Predicted Background and Their Mitigation
XENONnT projection

## Slide 11
Low energy β-decays from 222Rn is a major background in both ER and NR bands (via leakage)
Successful reduction of 222Rn drives the improvement on the final sensitivity
Strategy: AVOID or REMOVE
Shengchao Li | CoSSURF 2022 | May 13, 2022
11
Suppression of 222Rn background is the key
JCAP 11 (2020) 031

## Slide 12
Cleanliness procedures
Radioassay program:
  gamma-ray/mass spectrometry
  222Rn emanation measurement
Identify Rn source over subsystems
Rn emanation rate:
  4.2 µBq/kg (simulated)
2112.05629 [accepted EPJC]
1/3 of 1T level
Material Screening and Cleaning
Shengchao Li | CoSSURF 2022 | May 13, 2022
12

## Slide 13
Trap less volatile Rn until it decays
Separate Rn from Xe via vapor pressure difference
Cryogenic distillation
  Clean component
  Rn-free mag-pump
Can operate with both LXe and GXe
XENONnT strategy:
  2x with high flow distillation column for sources inside LXe
  2x by GXe extraction to remove Rn before entering TPC
EPJC 78 (2018) 604
EPJC 81 (2021) 337
EPJC (2017) 77 358
High Rn
Low Rn
Shengchao Li | CoSSURF 2022 | May 13, 2022
13
Radon Distillation Column
MagPump x4

## Slide 14
GXe-only mode shows Rn reduction:
3.3 µBq/kg -> 1.7 µBq/kg
Lowest 222Rn/Xe level in operating LXe TPC
Expect below 1µBq/kg with additional LXe mode
nT goal: 1 µBq/kg
222Rn/Xe = 10-25
Shengchao Li | CoSSURF 2022 | May 13, 2022
14
Radon Distillation Column Performance

## Slide 15
Gd-Water Cherenkov detector
33m3, with 120 PMTs inside ePTFE panels
87% expected neutron tagging efficiency with Gd-doped water
JCAP (2020) 11 031
Trigger on 4.4 MeV AmBe, 90% efficiency in detecting neutron capture with demi-water
Translate to 65% tagging efficiency with water (match with sim)
4.4 MeV from AmBe
2.2 MeV from 2H
Shengchao Li | CoSSURF 2022 | May 13, 2022
15
Neutron Veto System
Goal: <1 evt / (20 t × yr)

## Slide 16
XENONnT has been taking data consistently in triggerless mode (open-source package: strax, straxen)
PMTs have stable gains thanks to the LED calibration, average QE is 34%
Good single-electron resolution
 | Light collection | S1 resolution @41.5keV | S2 resolution
1T | 14% | 8% | 13.7%
nT* | 17% | 7.6% | 15.1%
*preliminary result
Shengchao Li | CoSSURF 2022 | May 13, 2022
16
Initial Science Run Performance

## Slide 17
220Rn
83mKr
AmBe
83mKr: spatial homogeneity and position dependent TPC response
220Rn: model low energy ER band
AmBe: model low energy NR band
Shengchao Li | CoSSURF 2022 | May 13, 2022
17
XENONnT Calibration Campaign

## Slide 18
4 tons fiducial volume with 5 year time span
SI WIMP sensitivity (90% C.L.):
  1.4×10−48 cm2 @ 50 GeV/c2
JCAP (2020) 11 031
Approaching designed exposure, both 222Rn and neutron background will have high impact to final sensitivity
Shengchao Li | CoSSURF 2022 | May 13, 2022
18
XENONnT Science Goals: WIMP Search

## Slide 19
The first few months of XENONnT data will either confirm or reject the excess with high significance
If the excess persists, we can differentiate hypothesis for its origin unambiguously:
  E.g., B0+ 3H +solar axion model v.s. B0+ 3H model at 5σ
Shengchao Li | CoSSURF 2022 | May 13, 2022
19
XENONnT Science Goals: ER Excess Investigation

## Slide 20
The “neutrino fog” is still far away with current iteration of WIMP experiments
Interesting neutrino physics emerges through 0νββ search and a variety of astrophysical sources
Generation-3 LXe TPC will be the ultimate multi-purpose observatory to advance new physics
Joining forces from LZ & XENON
2203.02309
(courtesy of K. Morå)
Shengchao Li | CoSSURF 2022 | May 13, 2022
20
What if XENONnT does not see dark matter?
G3 whitepaper [2203.02309]
500+ authors, 77 pages,
40 figures, 1262 references

## Slide 21
@xenonexperiment
http://xenonexperiment.org
XENONnT direct detection experiment will improve the current WIMP limit by more than an order of magnitude, and deliver better understandings on the ER excess.
The newly developed neutron veto, LXe purification system and radon distillation column after XENON1T will further suppress backgrounds in the detector.
The experiment has been taking data since 2020 in very stable condition, with the result from the initial science run to be released soon.
Stay tuned!
Shengchao Li | CoSSURF 2022 | May 13, 2022
21
Conclusions
xenon_experiment
XENONexperiment

## Slide 22
Shengchao Li | CoSSURF 2022 | May 13, 2022
22
Backup Slides

## Slide 23
Cryogenics system,
LXe/GXe purification,
Rn distillation column
Slow control,
Data acquisition
Online Kr distillation,
Xe recovery system
XENONnT Subsystems
Shengchao Li | CoSSURF 2022 | May 13, 2022
23

## Slide 24
Process speed at 8.3 slpm (=3kg/h)
Kr reduction factor of 104–105
Delivers final concentration level of < 48 ppq natKr/Xe in the system
Also useful for removing 37Ar after calibration
EPJC 77 (2017) 275
2112.12231
Kr, Ar
Xe
Krypton Distillation Column
Shengchao Li | CoSSURF 2022 | May 13, 2022
24

## Slide 25
8.9% abundance
136Xe 0:
SNEWS 2.0
R. Lang et al.
PRD (2016) 10 103009
2205.04158
XENONnT Science Goals: Neutrino Physics
Shengchao Li | CoSSURF 2022 | May 13, 2022
25