## Slide 1: Geotechnical Monitoring and structural support as part of the lbnf project
Presented by:
Brett E Belzer
Staff consultant, Rock Mechanics
2022

## Slide 2: Presentation overview
Pre excavation phase of the LBNF project
  Third party testing
  Noise and Vibration Monitoring
Main excavation phase of the lbnf project
  Geotechnical monitoring
    Multiple point borehole extensometers
    Inclinometers
    Seismographs
    Data Acquisition
  Structural Support Tasks

## Slide 3: Pre excavation phase of the LBNF project
Third party testing
  Rock Pull Testing UG
  Steel Inspections at Ross Shaft Headframe
    Magnetic particle
    Visual inspection
  Earthworks
    Density testing
    Concrete and grout testing
  Micropiles for conveyor bents

## Slide 4: Pre excavation phase of the LBNF project
Third party testing
  Micropiles for conveyor bents

## Slide 5: Pre excavation phase of the LBNF project
Noise and Vibration Monitoring
  OSHA 8-hour time weighted average (TWA) threshold of 85 dBA as an action level and 90 dBA as the permissible exposure limit (PEL)
  Instantel Minimate Pro 4 and Minimate microphone. Highest computed was 83.7 dBA

## Slide 6: main excavation phase of the LBNF project
Geotechnical Monitoring – 2021 to 2024
  Multiple point borehole extensometers (MPBX) x 64 total will be installed
  Inclinometers
  Seismographs

## Slide 7: Multiple point borehole extensometers
Multiple point borehole extensometers –Geokon Model 1250 A-5 with hydraulic anchors

## Slide 8: Multiple point borehole extensometers

## Slide 9: main excavation phase of the LBNF project
Multiple point borehole extensometer installation

## Slide 10: main excavation phase of the LBNF project
Multiple point borehole extensometer installation

## Slide 11: main excavation phase of the LBNF project
Central data management system
  Canary Systems MultiLogger and ML WEB are used to program the loggers
  ML Web is the user interface used to view and interpret the data
  Remote connection via VPN
  Geokon Model 8600-2 Dataloggers and Multiplexors
  Dataloggers read MPBX every 2 minutes

## Slide 12: main excavation phase of the LBNF project
Central data management system Canary ML WEB

## Slide 13: main excavation phase of the LBNF project
Inclinometers -Tilt Meter
  Geokon Model 6180 – 70 ft long
  Casing

## Slide 14: Noise and Vibration Monitoring
Seismographs

## Slide 15: Noise and Vibration Monitoring
Daily Reporting

## Slide 16: Noise and Vibration Monitoring
Daily Reporting

## Slide 17: Noise and Vibration Monitoring
Weekly Attenuation Reporting

## Slide 18: main excavation phase of the LBNF project
Structural support tasks
  Grizzly rock breaker foundation

## Slide 19: main excavation phase of the LBNF project
Structural support tasks
  Lift Reviews

## Slide 20: Structural Lift Reviews
Slings and Shackles checks
Lifting Steps
Vertical Cage Capacity – 13,500 lbs
Side Load Capacity of the Cage – 2,000 lbs

## Slide 21: Structural Lift Reviews
Zimmerman car
20-ft long CT Bolts

## Slide 22: Structural Lift Reviews
Zimmerman car
20-ft long CT Bolts

## Slide 23: Structural Lift Reviews
Zimmerman car
20-ft long CT Bolts
Test Pick

## Slide 24: Imagine having access to a think tank with hundreds of diversely talented engineers, scientists, programmers, and developers under one roof—that’s RESPEC. Questions?