## Slide 1
Accelerated carbon sequestration from thermophilic microbes
Magan Vaughn1, Jasmeet Kaur2, Tanvi Govil3, Dr. Rajesh Sani3, Dr. Bret Lingwall4
1Department of Chemistry, Biology and Health Sciences, South Dakota Mines, Rapid City, SD, USA; 2Department of Biotechnology and Bioinformatics, Jaypee University of Information Technology, Solan, India; 3Department of Chemical and Biological Engineering, South Dakota Mines, Rapid City, SD, USA; 4Department of Civil and Environmental Engineering, South Dakota Mines, Rapid City, SD, USA
Carbon Dioxide Sequestration
Carbon dioxide is a greenhouse gas and major contributor to climate change
Carbon dioxide dissociates in water into carbonate ions. In the presence calcium, magnesium and iron ions a solid, stable carbonate is formed.
This process can be accelerated through carbonic anhydrase producing microbes
Carbonic anhydrase converts carbon dioxide into carbonate ions
The Sanford Underground Research Facility (SURF) provides a unique environment to investigate novel carbonic anhydrase producing microbes
Extremophilic bacteria produce stable enzyme that can be used for carbon capture
Enrichment of SURF Samples for Carbonic Anhydrase
Analysis of Bacterium in SURF Group I
Sites and Samples used for this study
Acknowledgment
We are grateful for financial support from the National Science Foundation (NSF 2026: EAGER: Award # 2033577). Support from the Composite and Nanocomposite Advanced Manufacturing – Biomaterials Center (CNAM-Bio) is also acknowledged.
Ongoing Work
Our Goal
Explore Sanford Underground Research Facility (SURF) for novel carbonic anhydrase bacterium through metagenomics and meta-transcriptomics
Enrich SURF samples for carbonic anhydrase producing bacterium
Isolate bacteria and perform 16s colony PCR to determine bacteria present
Investigate the thermophilic bacterium Geobacillus sp. WSUCF1 for carbonic anhydrase production
Sanford Underground Research Facility, SD, USA
Figure 2: Carbonic anhydrase activity from SURF samples every 24 hours
Figure 4: Agarose gel electrophoresis on 16s colony PCR from isolated colonies
Figure 1: Growth of SURF samples every 24 hours
Carbonic Anhydrase Production of Geobacillus sp. WSUCF1
Table 2: Carbonic anhydrase activity from Geobacillus sp. WSUCF1 with different media
Completion of isolation from remaining SURF samples
Completion of metagenomic and meta-transcriptomics to understand
Meta-transcriptomics to understand the functional microbiome characteristics
L 1a 1b 2 3a 3b 3c 3d 3e 3f
L 3g 3h
Figure 3: Spread plate (left) of SURF Group I samples and isolated bacterium (right) from SURF Group I samples
Table 1: Species of bacteria
 | Species | Query Cover | Pecent Identitiy
1a | Bacillus subtilis | 85% | 96.89%
1b | Bacillus tequilensis | 88% | 95.40%
2 | Bacillus infantis | 79% | 97.35%
3a | Bacillus lichenformis | 82% | 94.23%
3b | Bacillus halotolerans | 88% | 95.19%
3c | Bacillus rugosus | 94% | 94.81%
3d | Bacillus cereus | 84% | 97.58%
3f | Bacillus velevzensis | 91% | 97.21%
3g | Bacillus megaterium | 91% | 96.79%
3h | Bacillus inaquosorum | 87% | 98.32%
Samples were collected from boreholes drilled in SURF
Samples were separated into four groups based on depth from bore hole
  Group I: 0-50 m
  Group II: 51-100 m
  Group III: 101-150
  Group IV: 151-200
Sanford Underground Research Facility, SD, USA
(SURF, 30C)