## Slide 1: DUNE Module of Opportunity (MooD) Workshop (Nov 2019)

## Slide 2
LBNF/DUNE will build two far detector modules
Excavated space for two additional modules (~17kt LAr equivalent)
2022 Update!
FD2: Vertical Drift
  CRP (France, US, CERN)
  TPC Electronics (France, Japan, US)
  PDS (US, Italy, Spain, Brazil, France)
  HV (US, CERN, France)
  DAQ (UK, CERN, Canada, US, Czech Republic)
  CALCI (US, Spain)
Charge Readout Planes (CRP)
Photon Detector System (PDS)
DAQ
Bottom Drift Electronics (BDE)
CALCI
HV
Top Drift Electronics (TDE)
FD1 : Horizontal Drift
FD1
FD2
new

## Slide 3: Project “Far Site” at Sanford Underground Research Facility (SURF) in Lead, SD
SURF is located at the former Homestake Gold Mine, in Lead SD
Property transferred to South Dakota Science and Technology Authority (SDSTA) to create and operate underground science facility
SDSTA operates SURF under a cooperative agreement with DOE-OHEP
DOE has leased areas for LBNF facilities from SDSTA; construction easements in place for access and temporary construction use
FRA has a memorandum of understanding with SDSTA with respect to LBNF/DUNE-US project support, services and responsibilities
Ross shaft headframe
Yates shaft headframe
new

## Slide 4
Excavation Completed
Excavation and Shotcrete Complete
May 6 2022
Temporary Concrete Batch Plant Location
Concrete Complete
Excavation Direction (Blue Team)
Excavation Direction (Red Team)
Total Excavation Complete 27%
West Access Drift
East Access Drift
Spray Chamber
Pilot Drift
South Access Drift
Cut 1
new

## Slide 5
new

## Slide 6
MooD workshop agenda
Main workshop sessions
LArTPC projective charge readout
LArTPC pixel charge readout
LArTPC light readout
Other technologies

## Slide 7: impressions of MooD workshop…
Many very interesting and exciting ideas
Compelling case for further development of noble liquid TPCs and other ideas
Generated enthusiasm and ideas
Development effort continues…
LBNF project will build an outstanding underground facility and beam:
  …there is space for additional detectors
  A clear need to advance detector development towards the Module(s) of Opportunity

## Slide 8: Progress since MooD
Vertical drift:
  Many ideas on charge and light readout are now implemented in FD2
  Vertical drift is a leading candidate for FD3-4
Pixels:
  Significant progress in pixel development with LArPIX for LAr-ND (see also SoLAr)
Theia, SoLAr, SLoMo
…

## Slide 9: Progress since MooD
Theia: An Advanced Optical Neutrino Detector
https://arxiv.org/pdf/1911.03501.pdf

## Slide 10: Progress since MooD
Theia: An Advanced Optical Neutrino Detector

## Slide 11: Progress since MooD
Low Background kT-Scale Liquid Argon Time Projection Chambers
https://arxiv.org/pdf/2203.08821.pdf
1-3 kton fiducial volume(s)
Acrylic box
SiPMs
Water shielding
Low background underground argon
Cryostat
Central cathode
Charge readout planes

## Slide 12
A Low Background DUNE-like Module: SLoMo* (SURF Low Background Module)
Eric Church
CoSSURF 2022
There is significant interesting physics to be done in large LArTPCs below current thresholds of ~10MeV.
physics
    Solar neutrino measurements
    Supernovae detection
    Supernovae Coherent n-Nuclear elastic scattering (CEvNS) “glow”
    0nbb search
    WIMP Dark Matter search
Might hope for module 3,4 for DUNE to look like this
  “DO NO HARM” to the main physics program

## Slide 13: Progress since MooD
SoLAr: Solar Neutrinos in Liquid Argon
https://arxiv.org/pdf/2203.07501.pdf

## Slide 14: Progress since MooD
Snowmass2021 - Letter of Interest
Q-Pix: Kiloton-scale pixelated liquid noble TPCs
https://www.snowmass21.org/docs/files/summaries/IF/SNOWMASS21-IF7_IF8-NF10_NF0_Jonathan_Asaadi-079.pdf
https://www.snowmass21.org/docs/files/summaries/IF/SNOWMASS21-IF7_IF8-NF10_NF0-UF3_UF0_Dan_Dwyer-171.pdf
Snowmass2021 Letter of Interest: An R&D Collaboration for
Scalable Pixelated Detector Systems
https://www.snowmass21.org/docs/files/summaries/NF/SNOWMASS21-NF10_NF0-IF9_IF8_Xin_Qian-123.pdf
Development of LArTPC Vertical Drift Solutions with
PCB Anode Readouts for DUNE
… many others

## Slide 15: … next steps
LBNF will complete excavation of the far site (for 4 detectors) in 2024
DUNE currently has resources to build two far detectors (FD1-horizontal drift and FD2-vertical drift). Expect completion in ~2029.
Natural to plan for R&D towards improvements for FD3-4.
Since MooD-2019 many ideas put forward in Snowmass
  LArTPC based on vertical drift
  LArTPC with pixel readout
  Low background combinations of noble liquids
  Water/scintillator-based detectors
Many ideas to add to the main DUNE program

## Slide 16: …next steps
Following successful MooD workshop at BNL in 2019
  DUNE is planning some followup:
    Collaboration meeting parallel session on Module of Opportunity next week (Thursday May 19 at 14:00 CDT).
    DUNE followup workshop in Spain (October?)
Feed Snowmass/P5 and international planning
Many stakeholders in addition to DUNE: DOE, SURF/SDSTA, FNAL,…
…

## Slide 17: Backup

## Slide 18: ARAPUCA Light Detection
Light Readout
Flavio
Denver
Xe doping
Reflective Foils
Andrzej, Marcin
X-arapuca developments
Xe-doping
Reflective foils
active signal ganging
large arrays of SiPMs
power over fiber (SiPM at HV)

## Slide 19: Vertical Drift LArTPC
First introduced at the CERN mini workshop in June 2019
Based on the simple assembly concept of DP field cage
6m drift, 300KV technology almost acquired.
Reduced purity requirements compared to 12m DP drift
Modular and easy to install
anode
anode
Cathode (300KV)
6m drift
6m drift
Unit = 3m x 3m
cryostat
Support wires
Charge Readout
Francesco
Dedicated R&D program at CERN carried out to replace LArTPC wire chamber with perforated multilayer printed circuit board (PCB). Fragile wires replaced by robust copper strips:
  Ionization electrons are focused through PCB holes
  Strips in front and intermediate layers sense induction signal
  Strips on last plane collect ionization electrons.
Idea was driven by improvements w.r.t. wire chambers:
  Components can be mass produced commercially
  Anode plane is robust, without risk of broken wires, simpler support structure
  Possibility of integrating FE electronics on PCB
  Better segmentation/modularity, test full readout before installation
  Take advantage of technological development of wide area Thick-Gems at CERN.

## Slide 20: Sourcing LRUA for DUNE could be a reality
DarkSide/Underground Ar
Cristiano, Eric
Argon is not generally looked for in underground gas fields
PNNL working with to explore large scale underground argon sources
  Supplier: Major U.S. gas producer/supplier (not disclosed at company request)
  Production rate: ~5,000 tonnes/year
    Can start in about 2 years
  Ballpark cost: x3 regular argon
  NOTE: These are very rough estimates.
  Further refinement require expression of true interest from DUNE
Next steps for physics:
  Reminder: DarkSide source is the only proven source (i.e., extremely low 39Ar)
  Measure 39Ar levels from new potential source
  For 42Ar level, new assay method required – expected to be VERY low
DarkSide: combined neutrino oscillation, dark matter and 0 experiment: LArTPC with 136Xe doping

## Slide 21: LArPix
Dan
LArPIX prototyping program for Near Detector
Deployment in ND-LAr
Ideas for FD module #4
Pixel readout ideas for LArTPC

## Slide 22: QPix
Mitch

## Slide 23: Intro to DUNE
Stefan

## Slide 24: LBNF/DUNE at Sanford Lab (SURF)
14 Jul 2020
Ross shaft headframe
Yates shaft headframe
4850L caverns and drift layout
18m
66m
Sanford Lab Reliability Projects FY16 – 20
  Ross shaft rehab
  Hoist motor rebuild, …
Pre-Excavation FY17 - 20
  Rock disposal systems
  Ross headframe
  upgrade, …
Excavation/ Construction FY21 – 24
  Brow/CUC/Drifts/Utilities/building/caverns
CD-3a Scope
Conventional Facilities:
  Surface and shaft Infrastructure
  Drifts and caverns for detectors
Cryostats & Cryogenics:
  Four membrane cryostats
  LN2 refrigeration system
  LAr purification systems
  70kt LAr
DUNE Detectors
  4 detectors