## Slide 1: The ARIADNE+ Program & Technology for DUNE
Kostas Mavrokoridis
(on behalf of the ARIADNE+ collaboration)
CoSSURF 2024, Rapid City, May 2024
k.mavrokoridis@liv.ac.uk
+
http://hep.ph.liv.ac.uk/ariadne

## Slide 2: Talk Outline
Background to the ARIADNE program
  TPX3Cam results taken with the ARIADNE+ 15-ton dual phase LAr detector at the CERN neutrino platform
Dual phase Optical protoDUNE run proposal
  Design progress and technical coordination
  Preparing the LoI to SPSC
ARIADNE: New results, 1-ton LAr run in Liverpool

## Slide 3: ARIADNE Detection Principle
ARIADNE has demonstrated light readout as a viable alternative to charge in dual-phase TPC neutrino experiments
Incoming particles ionise LAr and create prompt scintillation light (S1)
Electrons drift towards the extraction grid situated below the liquid level
A THGEM (THick-Gaseous Electron Multiplier) amplifies drift charge (capable of >30 kV/cm in LAr) generating secondary scintillation light (S2)
WLS (Wavelength Shifting) before imaging with ultrafast Timepix3 camera
ARIADNE (ARgon ImAging DetectioN chambEr)
Cameras
Benefits over previous charge readout techniques:
High resolution
Sensitivity to low energies
Very low noise, decoupled from TPC
Ease of access
Cost efficient
https://www.mdpi.com/2410-390X/4/4/35
https://iopscience.iop.org/article/10.1088/1748-0221/14/06/P06001
TPX3 provides simultaneous time-over-threshold (ToT) and time-of-arrival (ToA). Complete (x,y,z,E) event reconstruction using a single device.
Full 3D optical TPC

## Slide 4: ARIADNE at CERN T9
EMCCD data taking 3 weeks April 2018.
T9 Beamline, East Area, CERN.
Mix of particles: e ±, μ ±, π ±, p±. (0.5 – 8 GeV/c.)
43 cm
35 cm

## Slide 5: 2D -> Full 3D Optical Readout
Silicon pixel readout chip developed by the Medipix collaboration. Very well established technology at CERN.
Sensor resolution | 256x256 pixels
Pixel size | 55µm x 55µm
Max readout rate | 40Mhits•cm-2 •sec-1
Time resolution | 1.6 ns
TPX3 provides simultaneous time-over-threshold (ToT) and time-of-arrival (ToA). Complete (x,y,z,E) event reconstruction using a single device.
Time over threshold provides intensity / energy measurement ->10-bit resolution.
Time of arrival provides z (drift) axis position information -> 1.6 nanosecond resolution.
Data driven readout -> Event streaming with native zero suppression.
Efficient raw data storage. Triggerless operation.
TPX3 ASIC bonded to optical sensor

## Slide 6: TPX3Cam Optical Readout
Single photon sensitivity when combined with image intensifier.
Intensifier gain ~1E6 photons/photon.
Relay lens couples intensified image onto light sensitive
sensor which is bump bonded onto TPX3 ASIC.
Timepix3 camera installed in place of an EMMCD camera.
~ 30cm x 30cm field of view
Photonis Cricket image intensifier with Hi-QE green photocathode.
30% quantum efficiency at 430nm (TPB peak emission)
ARIADNE results
Coldbox Intensifier
TPB emission
Intensifier provides flexibility -> Many photocathode options are available to customise spectral sensitivity.
– Now also Direct VUV!

## Slide 7: TPX3Cam 3D Cosmics LAr
Continuous streaming, 10 msec slice (playing 1ms jump per frame)
Top View
Side View

## Slide 8: ARIADNE TPX3 Results
Stopping Muon
MIP Energy Calibration
https://www.mdpi.com/2410-390X/4/4/35
ADU (ToT) vs. THGEM Bias
11% energy resolution
Cameras are sensitive to the linear light production regime

## Slide 9: Module of Opportunity Workshops
Conceptual DUNE Dual Phase with Optical Readout
320 TPX4Cams within the cryostat chimneys
Each camera images 1.5mx1.5m with 3mm/pixel resolution
Total camera commercial cost with optics ~3M Euro
Camera type | Sen. Size (pixels) | Cameras to cover 1m2 | Resolution (mm/pix) | Total cameras (to cover 720m2) | Total cost (assuming €5k /camera*)
TPX3 | 256x256 | 9 | 1.3 (~ARIADNE) | 6480 | 32.4M
TPX3 | 256x256 | 4 | 2 | 2880 | 14.4M
TPX3 | 256x256 | 1 | 4 (~ARIADNE+) | 720 | 3.6M
TPX4 | 512x448 | 4 | 1 | 2880 | 14.4M
TPX4 | 512x448 | 1 | 2 | 720 | 3.6M
TPX4 | 512x448 | 0.66 (1.5m/cam) | 3 | 320 | 1.6M
Table: As an example, demonstration figures for use of TimePix within Dune - 720m2, 60m x 12m
* Cost is a place holder based on discussions with ASI, assumes large production. Intensifiers and optics will double total cost

## Slide 10
Larger Scale Demonstration at the CERN Neutrino Platform
CERN LOI: https://cds.cern.ch/record/2739360
Test optical readout on a scale relevant for DUNE using the existing cold box
Operation March/April 2022

## Slide 11: ARIADNE+: Cryostat Optical Configuration
TPX3 Camera
Assembly (1 x VUV)
Light Readout Plane (LRP)
Cathode
TPX3 Camera
Assembly (3 x visible)
Large scale test of ARIADNE optical readout principle for dual-phase LArTPCs.
Four Timepix3 based cameras, each covering 1m x 1m readout area.
Three cameras detect visible light (wavelength shifter installed above THGEMs)
One camera directly detects VUV.

## Slide 12: ARIADNE+: Cryostat Optical Configuration
20 cm electron drift
Reentrance viewports, cameras in gas nitrogen

## Slide 13: TPX3 Camera System
Timepix 3 Camera
Relay optics
Image intensifier
Objective lens

## Slide 14: Re-entrance Viewport
Visible lenses (f0.95, 10.5 mm)
Custom made VUV MgF2 Lens (f3, 11mm, 5mm diameter)

## Slide 15: Light Readout Plane (LRP) Design
Bottom view
Photochemically etched extraction grids
THGEMs/Extraction grids supported by PEEK Spacers
2.3m
16x 50cm square G-THGEMs
Welded Invar structure (Uniquely low coefficient of thermal contraction)
Modular design and can be applied directly to a DUNE module

## Slide 16: Light Readout Plane (LRP)
LRP assembly at CERN

## Slide 17: 50cm Glass THGEMs
Sixteen 50cm x 50cm glass THGEMs
1.1mm thick,
500μm ID holes,
800μm pitch hexagonal array
Novel Glass THGEMs developed at Liverpool (Patent accepted GB2019563.2)
See for more details:
https://www.mdpi.com/2076-3417/11/20/9450

## Slide 18: Glass THGEM Facility
Abrasive machining facility in the University of Liverpool physics building
Fully automated
Capable of machining 850mmx850mm active area
Not limited to glass, any brittle material i.e. ceramic, carbon fibre etc.
Will lead glass THGEM R&D
And capable of protoDUNE large scale THGEMs
G-THGEM with ITO electrodes and holes formed by abrasive machining.
G-THGEM: https://www.mdpi.com/2076-3417/11/20/9450

## Slide 19: Light Readout Plane
LRP CAD
LRP grids, G-THGEMs and WLS
2x2m LRP G-THGEMs from underneath
The 15mm modular extraction region provided a very stable extraction field!

## Slide 20: Cold box Integration

## Slide 21: Cold box Integration

## Slide 22: Closing the Detector

## Slide 23: Commissioning at CERN
3 weeks data collection

## Slide 24: Glass THGEM Light Gain Study
Visible intensifier
VUV Intensifier

## Slide 25: TPX3Cam Cosmics
cosmics 30 sec exposure
Energy Calibration
https://arxiv.org/pdf/2301.02530v2.pdf
Visible
VUV
(vignetting effect needs correction)
Visible intensifier:
VUV intensifier:

## Slide 26: ARIADNE+ Conclusions
Optical readout achieved with stable detector conditions has been demonstrated at the same scales as that for vertical drift tests (CERN Neutrino Platform Cold Box)
Dual phase extraction region very stable at large scale!
TPX3 and Glass THGEM technology is ready for deployment now
ProtoDUNE will be the natural platform to perform the next essential step
Zero suppressed readout (approx. few kbytes per event)
Raw data is natively 3D
Huge readout rates possible (80 MHits/s)
Easy access for swapping in/out technologies
Comparatively low cost to other readout methods
Same readout is possible for dual phase or gas TPCs
TPX3Cam TPC Benefits
High resolution with approx. 1 mm per pixel
Technology | Physics enables | TRL | Cost (DUNE 12mx60m FD) | R&D plans
TPX3 CAM | Very low energy threshold & excellent tracking | 9 | 7.2M (1 cam/m2, 4mm/pix) | Lens and image intensifier testing
LRP (GTHGEM Array) |  | 7-8 | 10M (assumes 14k/m2, mass production cost reduction is not included) | Larger scale tests (protoDUNE)
TPX4 CAM | Improved time & energy resolution | 7 | 3.2M (0.6 cam/m2, 3mm/pix) | Full characterization

## Slide 27: Using ProtoDUNE dual phase to test optical readouts for Neutrinos and DM; TPX3Cams, DarkSide type PDUs & X-Arapucas
Planned Proposal to SPSC:
TPX Cameras

## Slide 28
Two LRPs with glass THGEMs, similar to the ARIADNE cold box test
TPX3 Cams in the existing cryostat ports
Darkside PDUs, along the beam line
Modify partially existing field cage, with embedded X-ARAPUCAS in CT shape profile. Low energy threshold S1 (Flavio C et al)
ProtoDUNE dual phase instrumentation with optical readout
X-ARAPUCAs
Cathode remains middle of TPC
CRPs (or other technology)

## Slide 29
In dark green shade is the FoV of the TPX cameras(1mx1m) using the current cryostat ports
12 Darkside-20k type PDUs produced in the UK/Naples
X- Arapucas will be used to cover the field cage (sides only and retain the rest of the field cage). X-Arapucas in the Field cage are of high importance to correlate S2/S1 signals for DM
Cathode can remain in the middle
Space to test more optical sensors for very low energy thresholds such as Darkside20k SiPMs
TOP VIEW Optical protoDUNE
X-ARAPUCAs
TPX3Cams ports

## Slide 30: Design effort -LRP
One LRP to contain 6x5 Glass THGEMS (very similar design concept as the ARIADNE cold box test)
Made out of Invar
Similar size to a vertical drift CPR
Will hang from four top cryostat ports and will be able to move up down using the existing levelling motors
CAD Models By George Stavrakis

## Slide 31: Design effort –LRP FEA
CAD Models & FEA By George Stavrakis
FEA weight of LRP

## Slide 32: Design effort –LRP FEA
CAD Models & FEA By George Stavrakis
Max deflection 0.7mm
Hanging from four points under cryostat ports (not ideal positions)

## Slide 33: Design Effort -Assembly
Field cage support structure (hangs from cryostat ports)

## Slide 34: Design Effort -Assembly
First LRP installation (independently hangs from cryostat ports)

## Slide 35: Design Effort -Assembly
Second LRP (hangs also independently)

## Slide 36: Design Effort -Assembly
Cathode planes hangs from field cage structure
Custom made add on cathode holders (installed without any drilling).

## Slide 37: Design Effort -Assembly
Field cage installation (mixture of the old and new square X-ARAPUCAs)
(APEX, Flavio Cavanna et.al)

## Slide 38: ARIADNE 1-ton Run @Liverpool
ARIADNE run just finished, tested some of the proposed instrumentation for protoDUNE.
Three TPX cameras installed, with the remaining ¼ of the detector dedicated to Darkside SiPMs.
Measure the response of Darkside SiPMs to varying THGEM bias and determine the correct gain for ProtoDUNE operation (in collaboration with Naples)
Test different types of intensifier - one previously used on ARIADNE and the new intensifier on ARIADNE+
Test TPB coated glass for WLS instead of PEN - assessing difference in light quantity
Calibration gamma sources tests

## Slide 39: LAr Tracks with new G-THGEM

## Slide 40: Calibration sources on ARIADNE
SIPM tiles above the glass THGEM
Co60 Heatmap - 14 mins long
1sec stream gamma source
Individual 1.2 MeV gamma
0.5 msec

## Slide 41: Installing SiPM tiles on ARIADNE
2 SIPM tiles from Naples (Giuliana Fiorillo et al) installed in one of the ARIADNE ports.
To observe performance in a dual phase operation S2 light.
SIPM tiles above the glass THGEM
Breakdown voltage
SPE
S1
S2
THGEM@3.1kV, PDM bias @63.7 V

## Slide 42: Proposed Timeline
Testing of Darkside type SiPMs in ARIADNE ☑️
Design of LRPs/TPC for protoDUNE
2025
2026
2027
Installation of TPC components in ProtoDUNE
Facility at Liverpool for GTHGEM production
Finalise all LRP design and start procurement
Finalise all APEX FC design and start procurement
Start Run
VD Run End
2024
Submit LoI to SPSC/PBC

## Slide 43
The A. Team
Thank you

## Slide 44: Extra Slides

## Slide 45: TPX3 -> TPX4

## Slide 46
THGEM S2 light production
VUV (126nm) light produced through de-excitation of Argon gas. TPB Wavelength shifter above THGEM converts to 430nm.
At low field (<2kV/cm), S2 light production is linearly proportional to THGEM field. No charge gain. Very stable operation without discharges. No ion production.
At higher fields, electron multiplication occurs (Townsend avalanche).
Exponentially increasing S2 light production -> Improved sensitivity/threshold
Simulation

## Slide 47: G-THGEM Characterisation
THGEM charging behaviour
THGEM bias scan
Bi-conical holes lead to “upwards” charging over time.
Straight wall holes lead to “downwards” charging over time
The charging behaviour of fused silica THGEMs results in greater light production for the same applied field.
All circle hole glass THGEMs produced more light than the equivalent FR4 THGEM.
https://www.mdpi.com/2076-3417/11/20/9450

## Slide 48: PEN WLS
Two grades of TEONEX PEN foil investigated Q51 and Q53.
Thinner PEN consistently found to have a better conversion efficiency than thicker sheets (surface interaction).
Q51 consistently found to have a better conversion efficiency than Q53.
50cmx50cm Q51 25μm PEN film glued on glass panel

## Slide 49: Focusing VUV Intensifier using GAr TPC
+1mm
+2mm
+3mm
Spacer rings
MgF2 objective lens position is fixed into viewport.
Spacers change focal length position between objective lens and intensifier photocathode.
+2mm found produce sharpest image (in GAr).
Intensifier photocathode QE
Alphas from Am-241 in 1100mb pure argon

## Slide 50: ProtoDUNE new FCage
Drawing by G. Stavrakis

## Slide 51
ProtoDUNE cathode, X-ARAPUCAS